## Slide 1: ETSI ISG NFV SOL WG: Release 2 and 3 status
February 18, 2020
Thinh Nguyenphu
NFV-ONAP Contact,
Nokia
ONAP

## Slide 2: Outline
  PART 1: NFV Release 2
    What does it contain?
    Maintenance, API development, etc.
  PART 2: NFV Release 3
    Overview
    Features and specification work

## Slide 3: Part 1: NFV Release 2

## Slide 4: Release 2: protocols and data model standardization
The content of the NFV-SOL APIs is based on the related NFV-IFA and NFV-SEC specifications. The NFV-SOL specifications are implementable representations of the design defined in the stage 2 specifications, not alternative solutions.
Stage 2: Requirements and information model
NFV-IFA 007 (Or-Vnfm)
NFV-IFA 008 (Ve-Vnfm)
NFV-IFA 013 (Os-Ma-nfvo)
NFV-IFA 011 (VNF Package, VNFD)
NFV-IFA 014 (NSD and PNFD)
NFV-IFA 010 (NFV-MANO functional requirements)
Stage 3: Protocols and data model
NFV-SOL 003 (Or-Vnfm)
NFV-SOL 002 (Ve-Vnfm)
NFV-SOL 005 (Os-Ma-nfvo)
NFV-SOL 013 (Common API aspects)
NFV-SOL 004 (VNF Packaging and PNF archive)
NFV-SOL 001 (TOSCA VNFD, NSD)
NFV-SOL 006 (YANG VNFD, NSD)
NFV-SOL 007 (NSD file structure)
NFV-SOL 014 (Virtualised resource descriptors) (in draft)
NFV-SOL 016 (NFV-MANO procedures) (in draft)
Mapping information model to data model
Defining protocol machinery for the operations specified in stage 2
Closing gaps left open in stage 2 (e.g. error handling, technical details)
Testing: Benchmarking, interop, conformance
NFV-TST 007 (testing guidelines)
NFV-TST 010 (API conformance)
NFV-SOL 015 (NFV-MANO SOL API conventions and guidelines)
  OpenAPI descriptions for all APIs specified in GS NFV-SOL 002/003/005 (v2.6.1) https://nfvwiki.etsi.org/index.php?title=SOL_OpenAPI_Representations
  GS NFV-SOL 001/006 supporting files on ETSI Forge: https://nfvwiki.etsi.org/index.php?title=Deployment_Templates_and_Packaging_specifications
  Latest published versions: NFV-SOL001/002/003/004/005/006/007/013 v2.7.1 (Jan. 2020)
Security: requirements and IM
NFV-SEC 021 (VNF package security)
NFV-SEC 022 (API access token)

## Slide 5: Release 2: maintenance work
5 rounds completed (1H2017, published as v2.3.1; 2H2017, published as v2.4.1; 1H2018, published as v2.5.1, 2H2018 published as v2.6.1, and 2H2018 published as v2.7.1).
6th round, 1H2020 maintenance is ongoing (targeting publication of affected specifications as v2.8.1).
  With a deep focus on stage 3 specifications (NFV-SOL specs). Additional stage 2 specification on security has been considered for maintenance as well.
Main aspects addressed (so far) as part of maintenance:
  Correction of bugs and feedback from deployments and development: remove ambiguities, enhance APIs, etc.
  Alignment in between Stage 2 and 3 specifications.
  Security enhancements related to interfaces, descriptors and other artefacts.
  Extending constructs of VNF packaging for archiving files and artifacts of PNF.
  Feedback from open source projects, e.g., OpenStack gap analysis and alignment to NFV-IFA005 and NFV-IFA006, OSM information model feedback to NFV-IFA011 and NFV-IFA014, contributions to NFV-IFA011 and NFV-SOL004 by companies participating in ONAP providing feedback, etc.

## Slide 6: SOL001 ed271 key changes:
Generate a new yaml file, the etsi_nfv_sol001_common_types.yaml, which contains the common type definitions
Added support of the VNFFG design in the NSD model
Added support of Multiple NS deployment flavours design in the NSD model
Added support of nested NS design in the NSD model
Added support of NS monitoring design in the NSD model
Added support of dependencies design in the NSD model
Added support of VNF indicator design in the VNFD model based on tosca-simple-profile-yaml v1.3 notification feature
Differentiate the affiinityRule, AntiAffinityRule policies used in VNFD and NSD --> create new tosca.policies.nfv.NsAffinityRule and tosca.policies.nfv.NsAntiAffinityRule policy types only used in NSD
Differentiate the SecurityGroupRule policy used in VNFD and NSD --> create new tosca.policies.nfv.NsSecurityGroupRule policy type only used in NSD
Added support of virtual IP design in the VNFD model
Added the optional feature of using TOSCA imperative workflows when design a NSD
Added the informative mapping between the VNFD/NSD TOSCA model and the API attributes as defined by SOL002/SOL003/SOL005

## Slide 7: SOL004 ed271
A number of changes were performed to improve consistency which don’t introduce technical changes.
Add SEC022 support --> Mandatory signing of all artifacts

## Slide 8: SOL002 ed271 (1/2)
A number of changes were performed to improve consistency which don’t introduce technical changes.
VNF LCM API
Clarification that VNFM shall request the VIM to release the allocated resources in case of rollback of “InstantiateVnf”
Mandatory to return a 422 error when the testing of the notification endpoint has failed during subscription process
Clarify by which operations vnfConfigurableProperties can be modified
Expose the allowed maximum scale level per scaling aspect in the VnfInstance structure
Allow to pass vnfConfigurableProperties in the InstantiateVnfRequest
Clarify that external virtual links that are unchanged do not need to be passed in the ChangeVnfFlavourRequest and ChangeextVnfConnectivityRequest
Indicate that error information may be provided in VnfLcmOperationOccurrenceNotification and VnfLcmOpOcc also in case of “ROLLED_BACK” state
Deprecate the direct “UnresolvableFail” transition from "PROCESSING" into "FAILED" in the state model of an LCM operation occurrence
Add "vnfcResourceInfoId" attribute to VnfcInfo to clarify “id” of Type “VnfcResourceInfo”.
Add "vnfcInfoModifications" and "vnfcInfoModificationsDeleteIds“ to VnfInfoModificationRequest.
Fixed bugs of type of extCpInfo in VnfInstance to VnfExtCpInfo

## Slide 9: SOL002 ed271 (2/2)
VNF Performance management API
Remove the “Subscriptions” and “Individual subscription” resources. The management of callback information is now included in the management of thresholds and PM jobs, and is allowed to be updated with PATCH.
The way performance measurements are referenced has been updated to V 2.7.1 of the measurement specification (IFA027). As opposed to previous versions, a general model of structured measurements is now used that allows to use measured objects, or measured objects and related sub-objects
The two changes above constitute major, non-backwards-compatible changes which have led to updating the API version (semver) to V 2.0.0
VNF Fault management API
Mandatory to return a 422 error when the testing of the notification endpoint has failed during subscription process
Added an “alarmAcknowledgedTime” attribute to the “Alarm” data structure
Allowed to omit the “rootCauseFaultyResource” attribute in case the alarm does not affect virtualized resources
It is allowed now to reset an Alarm in “ACKNOWLEDGED” state to “UNACKNOWLEDGED” state
VNF Indicator API
Mandatory to return a 422 error when the testing of the notification endpoint has failed during subscription process
Clarify optional VNF indicator provided by VNF depends on VNF capability

## Slide 10: SOL003 ed271 (1/3)
A number of changes were performed to improve consistency which don’t introduce technical changes.
VNF LCM API
Clarification that VNFM shall request the VIM to release the allocated resources in case of rollback of “InstantiateVnf”
Mandatory to return a 422 error when the testing of the notification endpoint has failed during subscription process
Clarify by which operations vnfConfigurableProperties can be modified
Expose the allowed maximum scale level per scaling aspect in the VnfInstance structure
Allow to pass vnfConfigurableProperties in the InstantiateVnfRequest
Clarify that external virtual links that are unchanged do not need to be passed in the ChangeVnfFlavourRequest and ChangeextVnfConnectivityRequest
Indicate that error information may be provided in VnfLcmOperationOccurrenceNotification and VnfLcmOpOcc also in case of “ROLLED_BACK” state
Add a “zoneId” attribute to VnfcResourceInfo, VnfVirtualLinkResourceInfo andVirtualStorageResourceInfo to improve correlation of VnfInstance with information exchanged during granting
Add “resourceDefinitionId” and “zoneId” attributes to AffectedVnfc, AffectedVirtualLink and AffectedVirtualStorage to improve correlation of VnfInstance with information exchanged during granting
Deprecate the direct “UnresolvableFail” transition from "PROCESSING" into "FAILED" in the state model of an LCM operation occurrence

## Slide 11: SOL003 ed271 (2/3)
VNF Performance management API
Remove the “Subscriptions” and “Individual subscription” resources. The management of callback information is now included in the management of thresholds and PM jobs, and is allowed to be updated with PATCH.
The way performance measurements are referenced has been updated to V 2.7.1 of the measurement specification (IFA027). As opposed to previous versions, a general model of structured measurements is now used that allows to use measured objects, or measured objects and related sub-objects
The two changes above constitute major, non-backwards-compatible changes which have led to updating the API version (semver) to V 2.0.0
VNF Fault management API
Mandatory to return a 422 error when the testing of the notification endpoint has failed during subscription process
Added an “alarmAcknowledgedTime” attribute to the “Alarm” data structure
Allowed to omit the “rootCauseFaultyResource” attribute in case the alarm does not affect virtualized resources
It is allowed now to reset an Alarm in “ACKNOWLEDGED” state to “UNACKNOWLEDGED” state
VNF Indicator API
Mandatory to return a 422 error when the testing of the notification endpoint has failed during subscription process

## Slide 12: SOL003 ed271 (3/3)
Granting API
Clarify that external virtual links that are unchanged do not need to be passed in the granting response
VNF Pkgm API
Added full support for security information per individual artifact
Added full support for external artifacts
Allow definition of repository to download external artifacts from
Modified package state model
Added a resource that allows access to the VNF package manifest
Added support for bulk-fetching of artifacts
Added an attribute “onboardingFailureDetails” that allows to expose onboarding failure details
Mandatory to return a 422 error when the testing of the notification endpoint has failed during subscription process
The changes above constitute major, non-backwards-compatible changes which have led to updating the API version (semver) to V 2.0.0

## Slide 13: SOL005 ed271 (1/6)
NSD Management interface
In case of the Range header is present in the request and the NFVO does not support responding to range requests with a 206 response, it shall return a 200 OK response instead
The new value “ERROR” has been added to “PnfdOnboardingStateType” enumeration type. Updated the flow of the uploading of PNFD content
The new value “ERROR” has been added to “NsdOnboardingStateType” enumeration type. Updated the flow of the uploading of NSD content
Introduction of changes in the resource structure, new operations and changes in the existing operations of the NSD Management and PNFD Archive Management interfaces to support correctly the PNF Archive file and align the NSD file management, PNFD archive management and VNF Package management
PATCH method – the Content-Type header has been set to "application/merge-patch+json" according to IETF RFC 7396

## Slide 14: SOL005 ed271 (2/6)
NS Lifecycle Management interface
The “vnfConfigurableProperties” attribute has been added in “ParamsForVnf” and “InstantiateVnfData” data types
Alignment of LCM flows with SOL003
Addition of “locationConstraints” attribute in “InstantiateVnfData” data type and “additionalParam” attribute in “OperateVnfData” data type
Addition of the “id” attribute in some Notifications datatypes (NsIdentifierCreationNotification, NsInstanceDeletionNotification, NsChangeNotification)
Added 4 new attributes into “ParamsForVnf” data type

## Slide 15: SOL005 ed271 (3/6)
NS Performance Management interface
Added “objectType” and “subObjectInstanceIds” attributes in several data types to align with IFA027
Remove the “Subscriptions” and “Individual subscription” resources. The management of callback information is now included in the management of thresholds and PM jobs, and is allowed to be updated with PATCH.
The way performance measurements are referenced has been updated to V 2.7.1 of the measurement specification (IFA027). As opposed to previous versions, a general model of structured measurements is now used that allows to use measured objects, or measured objects and related sub-objects
The two changes above constitute major, non-backwards-compatible changes which have led to updating the API version to V 2.0.0
PATCH method – the Content-Type header has been set to "application/merge-patch+json" according to IETF RFC 7396

## Slide 16: SOL005 ed271 (4/6)
NS Fault Management interface
New “alarmAcknowledgedTime” attribute in “Alarm” data type
Mandatory to return a 422 error when the testing of the notification endpoint has failed during subscription process
Added an “alarmAcknowledgedTime” attribute to the “Alarm” data structure
Allowed to omit the “rootCauseFaultyResource” attribute in case the alarm does not affect virtualiz, ed resources
It is allowed now to reset an Alarm in “ACKNOWLEDGED” state to “UNACKNOWLEDGED” state
PATCH method – the Content-Type header has been set to "application/merge-patch+json" according to IETF RFC 7396
PATCH Method – the cardinality of ProblemDetails attribute has been changed from “0..1” to “1”

## Slide 17: SOL005 ed271 (5/6)
VNF Package Management interface
New “artifactUri” attribute in VnfPackageArtifactInfo data type
Addittion of the “vnfmInfo” attribute to “VnfPkgInfo” to expose useful metadata from the VNFD. Also add “vnfmInf”o from VNFD as an optional attribute to the VNF package onboarding notification and package management notifications filter
Introduction of the “artifactClassification” enumerated attribute in “VnfPackageArtifactInfo” data type that allows classifying artifacts
Addition of Oauth-type credentials for fetching external VNF packages in “UploadVnfPackageFromUriRequest” data type
Added API constructs to access the security information (resources “VNFD in an individual VNF package”, “Manifest in an individual VNF package”, “VNF package content”, “VNF package artifacts” and “Individual VNF package artifact) – GET method
In case of the Range header is present in the request and the NFVO does not support responding to range requests with a 206 response, it shall return a 200 OK response instead
Added normative statements of the steps to be taken after VNF package upload (PUT method)
The new value “ERROR” has been added to “PackageOnboardingStateType” enumeration type. New “onboardingFailureDetails” attribute has been added to “VnfPkgInfo” data type. The “ERROR” state has been added in VNF package state model.
Addition of the resource “Access configuration for external artifact download” (/ext_artifacts_access in the resource tree), flow and methods to provide and read access configuration information for the download of external artifacts

## Slide 18: SOL005 ed271 (6/6)
VNF Package Management interface (cont.)
Exposure of max scale levels through the addition of the “maxScaleLevels” attrite in the “instantiateVnfInfo” structure attribute of “VnfInstance” data type
Added the resource “VNF package artifacts” (“/artifacts” in the resource tree), flow and GET method for bulk-fetch artifacts that are not images
Added the “manifest of an individual VNF package” resource (“/manifest” in the resource tree), flow and GET method for reading the manifest of an on-boarded VNF package (for fetching the VNF package manifest)
New “nonManoArtifactSetId” attribute in “VnfPackageArtifactInfo” data type
PATCH method – the Content-Type header has been set to "application/merge-patch+json" according to IETF RFC 7396
All APIs:
In the POST method of the resource “Subscriptions” has been added the “ProblemDetails” attribute with response code “422 Unprocessable Entity”
Aligning API version indication with SOL015 - {apiRoot}/apiName/v1 to {apiRoot}/apiName/{apiMajorVersion}

## Slide 19: Release 2 ed281: stage 3: work plan
Reference | TB App
Propagated GSs | 
SOL001Ed281 “TOSCA based NFV Descriptors spec” | 2020-06-30
SOL002Ed281 "Ve-Vnfm RESTful protocols spec" | 2020-06-30
SOL003Ed281 "Or-Vnfm RESTful protocols spec" | 2020-06-30
SOL004Ed281 “VNF Package Stage 3” | 2020-06-30
SOL005Ed281 “Os-Ma –nfvo RESTful protocols spec” | 2020-06-30
SOL006Ed281 “NFV descriptors in YANG” | 2020-06-30
SOL007Ed281 “NSD file structure spec » | 2020-06-30
SOL013Ed281 “Common aspects of RESTful MANO APIs” | 2020-06-30

## Slide 20: Part 2: NFV Release 3

## Slide 21: Release 3: specification status
Stage 1 and 2:
  Stage 1 and 2 work has been completed, but some candidate features were closed or carried over to Release 4.
  Maintenance is ongoing: 1st round started 2H2019 (targeting publication as v3.4.1).
Stage 3:
  Stage 3 work is progressing to specify the set of stage 2 completed features.
  ETSI GS NFV-SOL 009 v3.3.1 and GS NFV-SOL 011 v3.3.1: First specifications as part of Release 3 have been completed and published.
  Other new NFV-SOL specification drafts related to Release 3 features are in progress (e.g., SOL010 and SOL012).
  Completion of first versions of evolved (from Rel. 2) SOL specs is planned also for the beginning of 2020. A “dropping” of stage 3 work will also be performed.

## Slide 22: Release 3: stage 1&2 completed features
  Compute Host Reservation
  NFV-MANO Policy Management Framework
  VNF Snapshots
  Management of NFV-MANO
  Network Service (NS) across multiple administrative domains
  Enhancement of acceleration related features:
    Hardware-independent acceleration
    Network acceleration for VNF
  Virtualization technologies:
    Hypervisor-based virtualisation
    Hardware environment for NFV
NFV-IFA specification versions:
Drop 1H2018 (drop #1)  v3.1.1
Drop 2H2018 (drop #2)  v3.2.1
Drop 1H2019 (drop #3)  v3.3.1
  VNF software modification
  Support of network slicing
  Management and connectivity for multi-site services.
Completed in 1H2018 (aka drop #1)
Completed in 2H2018 (aka drop #2)
Coloured in blue: more information on the backup slides
  NFVI software modification
  Service Availability Level (SAL)
Completed in 1H2019 (aka drop #3)

## Slide 23: Release 3 ed331: stage 3: work plan
Reference | TB App
Propagated GSs | 
SOL001Ed331 “TOSCA based NFV Descriptors spec” | 2020-03-31
SOL002Ed331 "Ve-Vnfm RESTful protocols spec" | 2020-03-31
SOL003Ed331 "Or-Vnfm RESTful protocols spec" | 2020-03-31
SOL004Ed331 “VNF Package Stage 3” | 2020-03-31
SOL005Ed331 “Os-Ma –nfvo RESTful protocols spec” | 2020-03-31
SOL006Ed331 “NFV descriptors in YANG” | 2020-03-31
SOL007Ed331 “NSD file structure spec » | 2020-03-31
SOL013Ed331 “Common aspects of RESTful MANO APIs” | 2020-03-31
New GSs | 
SOL009 “MANO mgmt stage 3“ | 2019.10.07
SOL010 “VNF snapshot pkg stage 3” | 2020-04-30
SOL011 “Or-Or Stage 3” | 2020-01-06
SOL012 “Policy Mgmt Intface” | 2020-04-28
New GRs | 
SOL017 “MSCS Stage 3” | 2020-04-30
The 1st publication of Release 3 GSs will not address all Release 3 features and might contain fixes agreed in IFAEd341. The minimum list of features required for the 1st publication: VNF software modification, Host Reservation; Network Slicing, Mgmt & Connectivity Multi-Site Services (MCMSS); VNF Snapshotting